The City of Belle Meade has adopted the 2009 residential code and all inspections will comply with that code.

The Building Official upon notification from the permit holder or his agent shall make or cause to be made any necessary inspections.  Inspections must be made with the Building Official during the hours of 8 a.m. and 4 p.m. Monday through Friday.  A MINIMUM OF 24 hour notice is required.

A grade marker with the average natural grade and finish grade is to be placed on the site before the footings are put in place and remain until the building official is satisfied that all grades are correct. Height of structure shall be checked from average natural grade once the highest rafters are in place.

Stamped approved plans must be on site during the construction and readily accessible to the inspector.

Erosion and sediment control practices, as indicated on City of Belle Meade approved plans, must be in place before construction is started and kept in place until completion of job or until erosion and sediment control measures are met.

Inspections for foundation, foundation walls, slabs, pools, pool slabs, sidewalks and driveways, shall be made after poles or piers are set or trenches or basement areas are excavated and any required forms erected and any required reinforcement is in place and prior to the placing of concrete.

Inspections for framing shall be made after the roof, all framing, firestopping, draft stopping, window flashing, bracing, are installed and the plumbing, mechanical and electrical rough inspections are approved and prior to the placement of the veneering.

Insulation shall not be in place at time of framing inspection.

Final inspections shall be made after the permitted work is completed and prior to occupancy. Occupying the structure before the issuance of a Certificate of Occupancy is prohibited. Contractors who allow owners to occupy a structure or part of a structure before the final inspection is approved, may be subject to withholding of new permits within the City of Belle Meade.

The Building Official may accept reports from approved agencies, provided such agencies satisfy the requirements as to qualifications and reliability. (check with building official first) reports and pictures must be submitted to the Building Official within 48 hours of the inspection.

It shall be the duty of the person doing the work authorized by a permit to notify the building official that such work is ready for inspection. It shall be the duty of the person requesting any inspection required by this code to provide access to and means for inspection of such work.

No contractor business advertising signs.    Grass must be kept cut and maintained.

As permit holder I have personally read and understand all of the requirements stated above.

Permit Holder:  							Date:

As Building Official I have discussed the above requirements with the permit holder.

Building Official: 							Date:

Work hours are Monday - Friday 7:00 a.m.-7:00 p.m.  Saturday 8:00 a.m.-5:00 p.m. No Sundays or federal holidays.